## Slide 1: Computer Networks Overview, Day 1
Mark Allman
mark.allman@case.edu
EECS 325/425
Fall 2018
“Oh, oh come take my hand,
We’re ridin’ out tonight to case the promise land...”

## Slide 2
2
All material copyright 2011—2018 Mark Allman, All rights reservered.
Acknowledgments:
- Several slides and ideas in this slide set come from Seth Hall.

## Slide 3: Our Scope
3

## Slide 4: Our Scope
3
This is a class in networking, which is a very broad topic

## Slide 5: Our Scope
3
This is a class in networking, which is a very broad topic
We will mostly focus on an artifact: the Internet

## Slide 6: Our Scope
3
This is a class in networking, which is a very broad topic
We will mostly focus on an artifact: the Internet
The Internet is not ....
  .... the only network
  .... the first network
  .... some sort of perfect realization of networking theory

## Slide 7: Our Scope
3
This is a class in networking, which is a very broad topic
We will mostly focus on an artifact: the Internet
The Internet is not ....
  .... the only network
  .... the first network
  .... some sort of perfect realization of networking theory
The Internet is the most pervasive and successful network

## Slide 8: What Is The Internet Anyway?!

## Slide 9: What is the Internet?
CAIDA’s IPv4 AS-level Internet Graph, February 2017

## Slide 10: What is the Internet?

## Slide 11: What is the Internet?

## Slide 12: What is the Internet?

## Slide 13: What is the Internet?

## Slide 14: What is the Internet?

## Slide 15: What is the Internet?

## Slide 16: What is the Internet?
12

## Slide 17: What is the Internet?
12

## Slide 18: What is the Internet?

## Slide 19: What is the Internet?
14

## Slide 20: What is the Internet?
14

## Slide 21: What is the Internet?
14

## Slide 22: What is the Internet?

## Slide 23: What is the Internet?

## Slide 24: What is the Internet?
17

## Slide 25: What is the Internet?
17

## Slide 26: What is the Internet?
17

## Slide 27: Scope Revisited
The scope of Internet use is massive
The scope of Internet technologies is massive
We cannot study them all in one semester
IP (v4 / v6)
TCP
DNS
BitTorrent
DHCP
NAT
End-to-end
principle
Fiber Optics
HTTP
Email
UDP
Late binding

## Slide 28: Scope (cont.)
19

## Slide 29: Scope (cont.)
19
Since we cannot cover everything we will focus on two areas.

## Slide 30: Scope (cont.)
19
Since we cannot cover everything we will focus on two areas.
  Fundamentals:
    key abstractions
    design criteria
    engineering tradeoffs

## Slide 31: Scope (cont.)
19
Since we cannot cover everything we will focus on two areas.
  Fundamentals:
    key abstractions
    design criteria
    engineering tradeoffs
  Exemplars:
    particular (common & crucial) protocols and services
    e.g., IP,TCP, DNS, HTTP, etc.

## Slide 32: Scope (cont.)
We will not be studying the nitty gritty of putting together of networks
  we will not learn to setup a cable modem
  we will not learn to configure a Cisco router
  we will not learn to assign static IP addresses to your Windows box
  we will not learn how to properly position your wireless access point
  we will not write web apps

## Slide 33: Scope (cont.)
21

## Slide 34: Scope (cont.)
21
You will end up with a rough understanding about how the Internet works

## Slide 35: Scope (cont.)
21
You will end up with a rough understanding about how the Internet works
  nobody really understands the entire system
    it is the most complex system mankind has ever engineered

## Slide 36: Scope (cont.)
21
You will end up with a rough understanding about how the Internet works
  nobody really understands the entire system
    it is the most complex system mankind has ever engineered
  expect me to say “I don’t know” on occasion
    or, even on many occasions!

## Slide 37: Comm. History
22

## Slide 38: Comm. History
22

## Slide 39: Comm. History (cont.)

## Slide 40: Comm. History (cont.)

## Slide 41: Comm. History (cont.)

## Slide 42: Comm. History (cont.)

## Slide 43: Comm. History (cont.)

## Slide 44: Comm. History (cont.)

## Slide 45: Circuit Switching
an
Allm
29

## Slide 46: Circuit Switching
an
Allm
29

## Slide 47: Circuit Switching

## Slide 48: Circuits (cont.)
Paul Baran
31

## Slide 49: Circuits (cont.)
Paul Baran
31

## Slide 50: Circuits (cont.)
Paul Baran
Ryan
31
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah

## Slide 51: Circuits (cont.)
Paul Baran
Ryan
31
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah
??
??
??
??
??

## Slide 52: Circuits-vs.-Packets
Ryan
32
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah
??
??
??
??
??

## Slide 53: Circuits-vs.-Packets
Ryan
32
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah
??
??
??
??
??

## Slide 54: Circuits-vs.-Packets
Ryan
33
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah
??
??
??
??
??

## Slide 55: Circuits-vs.-Packets
Ryan
33
Sarah
Ryan
Sarah
Sarah
Ryan
Sarah
??
??
??
??
??

## Slide 56: Layering
34

## Slide 57: Layering
34
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model

## Slide 58: Layering
34
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
OSI Model
Internet Model

## Slide 59: Layering (cont.)
35

## Slide 60: Layering (cont.)
35
Application
Transport
Network
Data Link
Physical

## Slide 61: Layering (cont.)
Application
Transport
Network
Data Link
Physical
35

## Slide 62: Layering (cont.)
36

## Slide 63: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical

## Slide 64: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical
signals

## Slide 65: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical
bits
signals

## Slide 66: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical
packets
bits signals

## Slide 67: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical
packets
packets bits signals

## Slide 68: Layering (cont.)
36
Application
Transport
Network
Data Link
Physical
data
packets packets bits signals

## Slide 69: Layering (cont.)
37

## Slide 70: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical

## Slide 71: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical
data

## Slide 72: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical
data
packets

## Slide 73: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical
data
packets packets

## Slide 74: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical
data
packets packets bits

## Slide 75: Layering (cont.)
37
Application
Transport
Network
Data Link
Physical
data
packets packets bits signals

## Slide 76: Layering (cont.)
38

## Slide 77: Layering (cont.)
38
Application
Transport
Network
Data Link
Physical

## Slide 78: Layering (cont.)
power, voltages, attenuation, etc.
38
Application
Transport
Network
Data Link
Physical

## Slide 79: Layering (cont.)
direct host-
to-host comm (e.g., ethernet)
38
Application
Transport
Network
Data Link
Physical

## Slide 80: Layering (cont.)
non-direct host- to-host comm (e.g.,
IP)
38
Application
Transport
Network
Data Link
Physical

## Slide 81: Layering (cont.)
process-to- process comm (e.g.,
TCP, UDP)
38
Application
Transport
Network
Data Link
Physical

## Slide 82: Layering (cont.)
app-to-app comm (e.g., HTTP, XMPP,
SMTP)
38
Application
Transport
Network
Data Link
Physical

## Slide 83: Layering (cont.)
39

## Slide 84: Layering (cont.)
39
Application
Transport
Network
Data Link
Physical

## Slide 85: Layering (cont.)
39
Application
Transport
Network
Data Link
Physical
} Electrical Engineering (Or, physics!)

## Slide 86: }
39
Layering (cont.)
Application
Transport
Network
Data Link
Physical
Computer Science
} Electrical Engineering (Or, physics!)

## Slide 87: }
39
Layering (cont.)
Application
Transport
Network
Data Link
Physical
Computer Science
} Computer Engineering
} Electrical Engineering (Or, physics!)

## Slide 88: Layering (cont.)
40

## Slide 89: Layering (cont.)
40
Application
Transport
Network
Data Link
Physical

## Slide 90: Layering (cont.)
40
Religion
Politics
Money
Application
Transport
Network
Data Link
Physical