## Slide 1: Application Layer Part 1
“All this energy callin’ me, back where it comes from; It’s such a crude attitude, back where it belongs”
Mark Allman
Case / ICSI
EECS 325/425
Fall 2018

## Slide 2
Allman
2
Many of these slides are more-or-less directly from the slide set developed by Jim Kurose and Keith Ross for their book “Computer Networking: A Top Down Approach, 5th edition”.
The slides have been lightly adapted for Mark Allman’s EECS 325/425 Computer Networks class at Case Western Reserve University.
All material copyright 1996-2010
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Reading Along ...
The application layer is covered in Chapter 2 of the book
Read for re-inforcement and depth of understanding
Allman
3

## Slide 4: Chapter 2: Application Layer
Our goals:
conceptual and implementation aspects of network application protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
learn about protocols by examining popular application-level protocols
  HTTP
  SMTP / POP3 / IMAP
programming network applications
  socket API

## Slide 5: Some network apps
e-mail
web
instant messaging
remote login
P2P file sharing
multi-user network games
streaming stored video (YouTube)
voice over IP
real-time video conferencing
cloud computing
 …
 …


## Slide 6: Creating a network app
write programs that
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
No need to write software for network-core devices
network-core devices do not
run user applications
 applications on end systems allows for rapid app development, propagation
Application 2-5

## Slide 7: Creating a network app
write programs that
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
No need to write software for network-core devices
network-core devices do not
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
run user applications
 applications on end systems allows for rapid app development, propagation
Application 2-5

## Slide 8: Creating a network app
write programs that
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
No need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
Application 2-5

## Slide 9: Reading Along ...
Allman
2.1: Principles of network applications
7

## Slide 10: Application architectures
client-server
peer-to-peer (P2P)
hybrid of client-server and P2P

## Slide 11: Client-server architecture
Application 2-8

## Slide 12: Client-server architecture
server:
always-on host
permanent IP address
server farms for scaling
Application 2-8

## Slide 13: Client-server architecture
server:
always-on host
permanent IP address
server farms for scaling clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
Application 2-8

## Slide 14: Client-server architecture
server:
always-on host
permanent IP address
server farms for scaling clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
client/server
Application 2-8

## Slide 15: Pure P2P architecture
Application 2-9

## Slide 16: Pure P2P architecture
peer-peer
Application 2-9

## Slide 17: Pure P2P architecture
 no always-on server
peer-peer
Application 2-9

## Slide 18: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peer-peer
Application 2-9

## Slide 19: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
 peers are intermittently connected and change IP addresses
peer-peer
Application 2-9

## Slide 20: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
 peers are intermittently connected and change IP addresses
highly scalable but difficult to manage
peer-peer
Application 2-9

## Slide 21: Hybrid of client-server and P2P
Application 2-10

## Slide 22: Hybrid of client-server and P2P
Skype
voice-over-IP P2P application
centralized server: finding address of remote party:
client-client connection: direct (not through server)
Application 2-10

## Slide 23: Hybrid of client-server and P2P
Skype
voice-over-IP P2P application
centralized server: finding address of remote party:
client-client connection: direct (not through server)
Instant messaging
chatting between two users is P2P
centralized service: client presence detection/ location
  user registers its IP address with central server when it comes online
  user contacts central server to find IP addresses of buddies
Application 2-10

## Slide 24: Processes communicating
Application 2-11

## Slide 25: Processes communicating
process: program running within a host.
within same host, two processes communicate using inter-process communication (defined by OS).
processes in different hosts communicate by exchanging messages
Application 2-11

## Slide 26: Processes communicating
process: program running within a host.
within same host, two processes communicate using inter-process communication (defined by OS).
processes in different hosts communicate by exchanging messages
Application 2-11
client process: process that initiates communication
server process: process that waits to be contacted

## Slide 27: Processes communicating
process: program running within a host.
within same host, two processes communicate using inter-process communication (defined by OS).
processes in different hosts communicate by exchanging messages
Application 2-11
client process: process that initiates communication
server process: process that waits to be contacted
 aside: applications with P2P architectures have client processes & server processes

## Slide 28: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door which brings message to socket at receiving process
process
TCP with buffers, variables
socket
host or server
process
socket
TCP with buffers, variables
host or server
Internet
controlled by OS
controlled by app developer
 API: (1) choice of transport protocol; (2) ability to fix a few parameters (lots more on this later)

## Slide 29: Addressing processes
to receive messages, process must have identifier
host device has unique 32- bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?

## Slide 30: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
 A: No, many processes can be running on same host

## Slide 31: Addressing processes
can be running on same host
 Port number: 80
Application 2-14
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
 A: No, many processes
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  Mail server: 25
to send HTTP message to www.icir.org web server:
 IP address: 192.150.187.12

## Slide 32: App-layer protocol defines
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send &
respond to messages
Application 2-15

## Slide 33: App-layer protocol defines
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
public-domain protocols:
defined in RFCs
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype

## Slide 34: What transport service does an app need?
Application 2-16

## Slide 35: What transport service does an app need?
Application 2-16
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, login) require 100% reliable data transfer

## Slide 36: What transport service does an app need?
Application 2-16
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, login) require 100% reliable data transfer
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”

## Slide 37: What transport service does an app need?
Application 2-16
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, login) require 100% reliable data transfer
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get

## Slide 38: What transport service does an app need?
Application 2-16
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, login) require 100% reliable data transfer
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
Security
encryption, data integrity,
…

## Slide 39: Transport service requirements of common apps
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video interactive games
instant messaging
Data loss
no loss no loss
no loss
loss-tolerant
loss-tolerant loss-tolerant
no loss
Throughput
elastic elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above few kbps up
elastic
Time Sensitive
no no
no
yes, 100’s msec
yes, few secs yes, 100’s msec
yes and no

## Slide 40: Internet transport protocols services
Application 2-18

## Slide 41: Internet transport protocols services
Application 2-18
TCP service:
connection-oriented: setup required between client and server processes
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantees, security

## Slide 42: Internet transport protocols services
minimum throughput guarantees, security
Application 2-18
TCP service:
connection-oriented: setup required between client and server processes
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing,
UDP service:
unreliable data transfer between sending and receiving process
does not provide: connection setup, reliability, flow control, congestion control, timing, throughput guarantee, or security

## Slide 43: Internet transport protocols services
minimum throughput guarantees, security
Application 2-18
TCP service:
connection-oriented: setup required between client and server processes
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing,
UDP service:
unreliable data transfer between sending and receiving process
does not provide: connection setup, reliability, flow control, congestion control, timing, throughput guarantee, or security
Q: why bother? Why is there a UDP?

## Slide 44: Internet apps: application, transport protocols
Application
e-mail
remote terminal access
Web
file transfer streaming multimedia
Application layer protocol
SMTP [RFC 2821]
Telnet [RFC 854], ssh
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube),
RTP [RFC 1889]
SIP, RTP, proprietary (e.g., Skype)
Underlying transport protocol
TCP TCP
TCP
TCP
TCP or UDP
Internet telephony typically UDP
Application 2-19