## Slide 1: Application Layer Part 4
Mark Allman
Case / ICSI
EECS 325/425
Fall 2018
“I don't really want to stop the show, But I thought that you might like to know,
That the singer's going to sing a song, And he wants you all to sing along.”

## Slide 2
Allman
Many of these slides are more-or-less directly from the slide set developed by Jim Kurose and Keith Ross for their book “Computer Networking: A Top Down Approach, 5th edition”.
The slides have been lightly adapted for Mark Allman’s EECS 325/425 Computer Networks class at Case Western Reserve University.
All material copyright 1996-2010
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Beyond Basic HTTP
Allman
HTTP is a big protocol / ecosystem with many extensions and variants
Let’s consider a few examples (not exhaustive in any way)

## Slide 4: HTTP request message: general format
Application 2-30

## Slide 5: HTTP request message: general format
Application 2-30

## Slide 6: HTTP request message: general format
b
HEAD method: asks server to leave requested object
out of response
Application 2-30

## Slide 7: HTTP response message
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
Application 2-33

## Slide 8: HTTP response message
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
Application 2-33

## Slide 9: Conditional GET
Application 2-44
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified

## Slide 10: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
Application 2-44

## Slide 11: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
Application 2-44

## Slide 12: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
object modified before
<date>
Application 2-44

## Slide 13: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object modified before
<date>
Application 2-44

## Slide 14: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object modified before
<date>
HTTP request msg
If-modified-since: <date>
Application 2-44

## Slide 15: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object modified before
<date>
HTTP request msg
If-modified-since: <date>
Application 2-44
object modified after
<date>

## Slide 16: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up- to-date:
HTTP/1.0 304 Not
Modified
client
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object modified before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
Application 2-44
object modified after
<date>

## Slide 17: Web caches (proxy server)
client
origin server
Goal: satisfy client request without involving origin server
origin server
Proxy server
client
Application 2-39

## Slide 18: Web caches (proxy server)
 user sets browser: Web accesses via cache
Goal: satisfy client request without involving origin server
client
Proxy server
client
origin server
origin server
Application 2-39

## Slide 19: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
Goal: satisfy client request without involving origin server
client
Proxy server
client
origin server
origin server
Application 2-39

## Slide 20: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy server
client
origin server
origin server
Application 2-39

## Slide 21: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy server
client
origin server
origin server
HTTP request
HTTP response
HTTP request
HTTP response
Application 2-39

## Slide 22: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy server
client
HTTP request
HTTP response
origin server
origin server
HTTP request
HTTP response
HTTP request
HTTP response
Application 2-39

## Slide 23: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Application 2-40

## Slide 24: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Application 2-40
why Web caching?

## Slide 25: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Application 2-40
why Web caching?
 reduce response time for client request

## Slide 26: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Application 2-40
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link.

## Slide 27: More about Web caching
cache acts as both client and server
typically cache is installed by ISP (university, company, residential ISP)
Application 2-40
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link.
Internet dense with caches: enables “poor” content providers to effectively deliver content

## Slide 28: Caching example
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 29: Caching example
assumptions
average object size = 100,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 30: Caching example
assumptions
average object size = 100,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
consequences
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 31: Caching example
assumptions
average object size = 100,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
consequences
utilization on LAN = 15%
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 32: Caching example
assumptions
average object size = 100,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
consequences
utilization on LAN = 15%
utilization on access link = 100%
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 33: Caching example
assumptions
average object size = 100,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
consequences
utilization on LAN = 15%
utilization on access link = 100%
 total delay = Internet delay + access delay + LAN delay
= 2 sec + seconds + milliseconds
origin servers
public Internet
institutional network
Application 2-41
10 Mbps LAN
1.5 Mbps access link

## Slide 34: Caching example (cont)
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 35: Caching example (cont)
possible solution
 increase bandwidth of access link to, say, 10 Mbps
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 36: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 10 Mbps
consequence
utilization on LAN = 15%
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 37: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 10 Mbps
consequence
utilization on LAN = 15%
utilization on access link = 15%
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 38: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 10 Mbps
consequence
utilization on LAN = 15%
utilization on access link = 15%
Total delay = Internet delay + access delay + LAN delay
= 2 sec + msecs + msecs
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 39: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 10 Mbps
consequence
utilization on LAN = 15%
utilization on access link = 15%
Total delay = Internet delay +
access delay + LAN delay
= 2 sec + msecs + msecs
 often a costly upgrade
origin servers
public Internet
institutional network
Application 2-42
10 Mbps LAN
10 Mbps access link

## Slide 40: Caching example (cont)
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 41: Caching example (cont)
possible solution:
 install cache
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 42: Caching example (cont)
possible solution:
install cache
consequence
suppose hit rate is 0.4
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 43: Caching example (cont)
possible solution:
install cache
consequence
suppose hit rate is 0.4
  40% requests will be satisfied almost immediately
  60% requests satisfied by origin server
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 44: Caching example (cont)
possible solution:
install cache
consequence
suppose hit rate is 0.4
  40% requests will be satisfied almost immediately
  60% requests satisfied by origin server
utilization of access link reduced to 60%, resulting in negligible delays (say 10 msec)
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 45: Caching example (cont)
possible solution:
install cache
consequence
suppose hit rate is 0.4
  40% requests will be satisfied almost immediately
  60% requests satisfied by origin server
utilization of access link reduced to 60%, resulting in negligible delays (say 10 msec)
 total avg delay = Internet
delay + access delay + LAN
delay = 0.6*2 secs +
0.4*milliseconds < 1.4 secs
origin servers
public Internet
institutional network
Application 2-43
10 Mbps LAN
1.5 Mbps access link
institutional cache

## Slide 46: HTTP connections
basic HTTP
 one object sent over TCP connection
Application 2-24

## Slide 47: HTTP connections
basic HTTP
 one object sent over TCP connection
Application 2-24
persistent HTTP
 multiple objects can be sent over single TCP connection between client, server.

## Slide 48: Non-Persistent HTTP: Response time
Application 2-27

## Slide 49: Non-Persistent HTTP: Response time
Application 2-27
definition of RTT: time for a small packet to travel from client to server and back.

## Slide 50: Non-Persistent HTTP: Response time
Application 2-27
definition of RTT: time for a small packet to travel from client to server and back.
response time:
 one RTT to initiate TCP connection

## Slide 51: Non-Persistent HTTP: Response time
Application 2-27
definition of RTT: time for a small packet to travel from client to server and back.
response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return

## Slide 52: Non-Persistent HTTP: Response time
Application 2-27
definition of RTT: time for a small packet to travel from client to server and back.
response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time total = 2RTT+transmit time

## Slide 53: Non-Persistent HTTP: Response time
definition of RTT: time for a small packet to travel from client to server and
back. response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time total = 2RTT+transmit time
time to transmit file
initiate TCP connection
RTT
request file
RTT
file received
Application 2-27
time
time

## Slide 54: Persistent HTTP
Application 2-28
non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects

## Slide 55: Persistent HTTP
Application 2-28
non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
persistent HTTP
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects