## Slide 1: Transport Layer Part 4
“Got my 45 on …
…so I …
… can rock on”
Mark Allman
mallman@case.edu
EECS 325/425
Fall 2018

## Slide 2
Allman
These slides are more-or-less directly from the slide set developed by Jim Kurose and Keith Ross for their book “Computer Networking: A Top Down Approach, 5th edition”.
The slides have been lightly adapted for Mark Allman’s EECS 325/425 Computer Networks class at Case Western Reserve University.
All material copyright 1996-2010
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Traffic By Protocol
CCZ, Sept. 10 2018
3
Allman

## Slide 4: Traffic By Protocol
CCZ, Sept. 10 2018
3
Allman

## Slide 5: Traffic By Protocol
TCP
UDP
CCZ, Sept. 10 2018
3
Allman

## Slide 6: Traffic By Protocol
TCP
UDP
Bytes
856.2 GB
~89%
102.8 GB
~11%
CCZ, Sept. 10 2018
3
Allman

## Slide 7: Traffic By Protocol
TCP
UDP
856.2 GB
~89%
102.8 GB
~11%
Bytes Connections
1.7 M
~53%
1.5 M
~47%
CCZ, Sept. 10 2018
3
Allman

## Slide 8: Reading Along ...
3.5: Connection- oriented transport:TCP
Allman
4

## Slide 9: TCP: Overview

## Slide 10: TCP: Overview
 point-to-point:
 one sender, one receiver

## Slide 11: TCP: Overview
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”

## Slide 12: TCP: Overview
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size

## Slide 13: TCP: Overview
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 14: TCP: Overview
full duplex data:
 bi-directional data flow in same connection
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 15: TCP: Overview
full duplex data:
 bi-directional data flow in same connection
 connection-oriented:
 handshaking inits sender, receiver state before data exchange
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 16: TCP: Overview
full duplex data:
 bi-directional data flow in same connection
connection-oriented:
  handshaking inits sender, receiver state before data exchange
congestion controlled:
  won’t overwhelm network
  (tackle later in semester)
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 17: TCP: Overview
full duplex data:
 bi-directional data flow in same connection
connection-oriented:
  handshaking inits sender, receiver state before data exchange
congestion controlled:
  won’t overwhelm network
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers
 (tackle later in semester)
flow controlled:
 won’t overwhelm receiver
Transport Layer

## Slide 18: TCP: Overview
full duplex data:
 bi-directional data flow in same connection
connection-oriented:
  handshaking inits sender, receiver state before data exchange
congestion controlled:
  won’t overwhelm network
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers
RFCs: 793, 1122, 1323, 2018, 2883,
3042, 3390, 5681, 6298, 6675, etc
 (tackle later in semester)
flow controlled:
 won’t overwhelm receiver
Transport Layer

## Slide 19: Reading Along ...
Allman
3.5: Connection- oriented transport:TCP
  segment structure
6

## Slide 20: TCP Segment Structure

## Slide 21: TCP Segment Structure

## Slide 22: TCP Segment Structure

## Slide 23: TCP Segment Structure

## Slide 24: TCP Segment Structure

## Slide 25: TCP Segment Structure

## Slide 26: TCP Segment Structure

## Slide 27: TCP Segment Structure

## Slide 28: TCP Segment Structure

## Slide 29: TCP Segment Structure

## Slide 30: TCP Segment Structure

## Slide 31: TCP Segment Structure

## Slide 32: TCP Segment Structure

## Slide 33: TCP Segment Structure

## Slide 34: TCP Segment Structure

## Slide 35: TCP Segment Structure

## Slide 36: TCP Segment Structure

## Slide 37: TCP seq. #’s and ACKs

## Slide 38: TCP seq. #’s and ACKs
Seq. #’s:
 byte stream “number” of first byte in segment’s data

## Slide 39: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK

## Slide 40: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments

## Slide 41: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments
A: TCP spec doesn’t say, - up to implementor

## Slide 42: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments
A: TCP spec doesn’t
Host A
Host B
time
simple telnet scenario
say, - up to implementor

## Slide 43: TCP seq. #’s and ACKs
Transport Layer
3-
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments
A: TCP spec doesn’t say, - up to implementor
User types ‘C’
Host A
Host B
time
simple telnet scenario

## Slide 44: TCP seq. #’s and ACKs
Transport Layer
3-
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments
A: TCP spec doesn’t say, - up to implementor
Seq=42, ACK=79, data = ‘C’
User types ‘C’
Host A
Host B
time
simple telnet scenario

## Slide 45: TCP seq. #’s and ACKs
Transport Layer
3-
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out- of-order segments
A: TCP spec doesn’t say, - up to implementor
Seq=42, ACK=79, data = ‘C’
User types ‘C’
host ACKs receipt of ‘C’, echoes back ‘C’
Host A
Host B
time
simple telnet scenario

## Slide 46: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
cumulative ACK
Q: how receiver handles out-
Seq=42, ACK=79, data = ‘C’
User types ‘C’
host ACKs receipt of ‘C’, echoes back ‘C’
Seq=79, ACK=43, data = ‘C’
Host A
Host B
of-order segments
 A: TCP spec doesn’t say, - up to implementor
time
simple telnet scenario

## Slide 47: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
 cumulative ACK
Seq=42, ACK=79, data = ‘C’
User types ‘C’
host ACKs
receipt
Q: how receiver handles out- of echoed
host ACKs receipt of ‘C’, echoes back ‘C’
Seq=79, ACK=43, data = ‘C’
Host A
Host B
‘C’
of-order segments
 A: TCP spec doesn’t say, - up to implementor
time
simple telnet scenario

## Slide 48: TCP seq. #’s and ACKs
Seq. #’s:
byte stream “number” of first byte in segment’s data
ACKs:
seq # of next byte expected from other side
 cumulative ACK
Seq=42, ACK=79, data = ‘C’
Seq=43, ACK=80
User types ‘C’
host ACKs
receipt
Q: how receiver handles out- of echoed
host ACKs receipt of ‘C’, echoes back ‘C’
Seq=79, ACK=43, data = ‘C’
Host A
Host B
‘C’
of-order segments
 A: TCP spec doesn’t say, - up to implementor
time
simple telnet scenario

## Slide 49: Reading Along ...
Allman
3.5: Connection- oriented transport:TCP
  connection management
9

## Slide 50: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
seq. #s
buffers, flow control info (e.g. RcvWindow)
etc.

## Slide 51: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
seq. #s
buffers, flow control info (e.g. RcvWindow)
etc.
Three way handshake:

## Slide 52: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
seq. #s
buffers, flow control info (e.g. RcvWindow)
etc.
Three way handshake:
Step 1: client host sends TCP SYN segment to server
specifies initial seq #
no data

## Slide 53: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
seq. #s
buffers, flow control info (e.g. RcvWindow)
etc.
Three way handshake:
Step 1: client host sends TCP SYN segment to server
specifies initial seq #
no data
Step 2: server host receives SYN, replies with SYNACK segment
server allocates buffers
specifies server initial seq. #

## Slide 54: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
seq. #s
buffers, flow control info (e.g. RcvWindow)
etc.
Three way handshake:
Step 1: client host sends TCP SYN segment to server
specifies initial seq #
no data
Step 2: server host receives SYN, replies with SYNACK segment
server allocates buffers
specifies server initial seq. # Step 3: client receives SYNACK,
replies with ACK segment, which may contain data

## Slide 55: TCP Connection Management (cont.)

## Slide 56
TCP Connection Management (cont.)
Closing a connection:

## Slide 57: TCP Connection Management (cont.)
Closing a connection:
client closes socket:
close(sd);

## Slide 58: TCP Connection Management (cont.)
Closing a connection:
client closes socket:
close(sd);
Step 1: client end system sends TCP FIN control segment to server

## Slide 59: TCP Connection Management (cont.)
Closing a connection:
client closes socket:
close(sd);
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.

## Slide 60: TCP Connection Management (cont.)
Closing a connection:
client closes socket:
close(sd);
Step 1: client end system sends TCP FIN control
segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 61: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
 Enters “timed wait” - will respond with ACK to received FINs
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 62: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
 Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 63
TCP Connection Management (cont)
TCP client lifecycle

## Slide 64
TCP Connection Management (cont)
TCP server lifecycle

## Slide 65: Reading Along ...
Allman
3.5: Connection- oriented transport:TCP
  timeouts
15

## Slide 66: TCP Timeouts and the RTT

## Slide 67
TCP Timeouts and the RTT
Q: How to set TCP timeout value?

## Slide 68: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
 longer than RTT …

## Slide 69: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies

## Slide 70
Measured RTTs
ping measurements from eecslab-5

## Slide 71: Measured RTTs
ping measurements from eecslab-5
Remote Host RTT (msec)

## Slide 72: Measured RTTs
ping measurements from eecslab-5
Remote Host
RTT (msec)
eecslab-6.case.edu
0.5

## Slide 73: Measured RTTs
ping measurements from eecslab-5
Remote Host RTT (msec) | 
eecslab-6.case.edu www.ohiou.edu | 0.5
 | 7.9

## Slide 74: Measured RTTs
ping measurements from eecslab-5
Remote Host RTT (msec) | 
eecslab-6.case.edu www.ohiou.edu www.icir.org | 0.5
 | 7.9
 | 71

## Slide 75: Measured RTTs
ping measurements from eecslab-5
Remote Host | RTT (msec)
eecslab-6.case.edu | 0.5
www.ohiou.edu | 7.9
www.icir.org | 71
www.iij.ad.jp | 171

## Slide 76: TCP Timeouts and the RTT

## Slide 77: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies

## Slide 78: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies
Q: What if we set the timeout too short?

## Slide 79: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies
Q: What if we set the timeout too short?
premature timeout
unnecessary retransmissions

## Slide 80: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies
Q: What if we set the timeout too short?
premature timeout
unnecessary retransmissions
Q: What if we set the timeout too long?

## Slide 81: TCP Timeouts and the RTT
Q: How to set TCP timeout value?
longer than RTT …
… but RTT varies
Q: What if we set the timeout too short?
premature timeout
unnecessary retransmissions
Q: What if we set the timeout too long?
slow reaction to loss

## Slide 82: TCP Timeouts and the RTT

## Slide 83
TCP Timeouts and the RTT
Q: How do we estimate the RTT?

## Slide 84: TCP Timeouts and the RTT
Q: How do we estimate the RTT?
 measure time between data transmission and ACK

## Slide 85: TCP Timeouts and the RTT
Q: How do we estimate the RTT?
Measure time between data transmission and ACK
do not time retransmissions
  (Karn/Partridge algorithm)

## Slide 86: TCP Timeouts and the RTT
Q: How do we estimate the RTT?
Measure time between data transmission and ACK
do not time retransmissions
  (Karn/Partridge algorithm)
RTT will vary across measurements

## Slide 87: TCP Timeouts and the RTT
Q: How do we estimate the RTT?
Measure time between data transmission and ACK
do not time retransmissions
  (Karn/Partridge algorithm)
RTT will vary across measurements
want something smoother
instead of just the current RTT, use an average of the last few measurements
the “smoothed RTT” (SRTT)

## Slide 88: TCP RTO
 RFC 6298
SRTT = (1- )*SRTT + *R
Exponential weighted moving average
influence of past sample decreases exponentially fast
standard value:  = 0.125

## Slide 89: Example SRTT Computation

## Slide 90: TCP RTO

## Slide 91: TCP RTO
Setting the timeout
 SRTT plus “safety margin”
 large variation in SRTT -> larger safety margin

## Slide 92: TCP RTO
Setting the timeout
SRTT plus “safety margin”
 large variation in SRTT -> larger safety margin
first, estimate of how much SRTT deviates from the RTT sample:

## Slide 93: TCP RTO
Setting the timeout
SRTT plus “safety margin”
 large variation in SRTT -> larger safety margin
first, estimate of how much SRTT deviates from the RTT sample:
RTTVAR = (1-)*RTTVAR + *|R-SRTT|
( = 0.25, per standard)

## Slide 94: TCP RTO
Setting the timeout
SRTT plus “safety margin”
 large variation in SRTT -> larger safety margin
first, estimate of how much SRTT deviates from the RTT sample:
RTTVAR = (1-)*RTTVAR + *|R-SRTT|
( = 0.25, per standard)
Then set timeout interval:
RTO = SRTT + 4*RTTVAR

## Slide 95: Example RTO Computation

## Slide 96: TCP RTO

## Slide 97
TCP RTO
But, one issue remains ...

## Slide 98: TCP RTO
But, one issue remains ...
 where do we start?!

## Slide 99: TCP RTO
But, one issue remains ...
where do we start?!
RFC 1122, RFC 2988 specify 3 seconds
why?

## Slide 100: TCP RTO
But, one issue remains ...
where do we start?!
RFC 1122, RFC 2988 specify 3 seconds
why?
RFC 1122 published in 1989. RFC 2988
published in 2000.

## Slide 101: TCP RTO
But, one issue remains ...
where do we start?!
RFC 1122, RFC 2988 specify 3 seconds
why?
RFC 1122 published in 1989. RFC 2988
published in 2000.
does this constant still apply?

## Slide 102: TCP Initial RTO

## Slide 103: TCP Initial RTO
Matt Sargent
Case PhD, 2015

## Slide 104: TCP Initial RTO
Matt Sargent
Case PhD, 2015
Hypothesizes that an initial RTO developed in 1989 might not be appropriate anymore
Conducts an empirical investigation

## Slide 105: TCP Initial RTO

## Slide 106
TCP Initial RTO
How do we choose?

## Slide 107: TCP Initial RTO
How do we choose?
look at some data!
investigated eight datasets (spanning 6 years)
datasets are packet traces!

## Slide 108: TCP Initial RTO
How do we choose?
look at some data!
investigated eight datasets (spanning 6 years)
datasets are packet traces!
Lowering the InitRTO from 3 seconds to 1 second has cost:
.... less than 0.1% of the connections spuriously retransmit the SYN in most datasets
.... 1.1% of the connections in a wireless network spuriously retransmit the SYN

## Slide 109: TCP Initial RTO

## Slide 110: TCP Initial RTO
Connections experience performance boost when SYN is lost and requires retransmission
i.e., connections only wait for 1sec when previously waited 3sec

## Slide 111: TCP Initial RTO
Connections experience performance boost when SYN is lost and requires retransmission
i.e., connections only wait for 1sec when previously waited 3sec
Connections realizing >= 10% boost:
10-43% (across datasets)
Connections realizing >= 50% boost:
17-73% (across datasets)

## Slide 112: TCP Initial RTO
The IETF decided that Matt’s evidence was compelling
The initial RTO was lowered from 3sec to 1sec
 specified in RFC 6298
Details of Matt’s investigation are given in appendix of RFC 6298

## Slide 113: TCP RTO

## Slide 114: TCP RTO
One more thing ...
What if we retransmit and the resent segment is dropped?

## Slide 115: TCP RTO
One more thing ...
What if we retransmit and the resent segment is dropped?
Backoff the RTO
RTO *= 2
(similar to collision backoff in Ethernet)
Part of TCP’s congestion control mechanism

## Slide 116: Magic Numbers

## Slide 117: Magic Numbers
Where do the constants in the RTO mechanism come from?
 e.g., alpha = 0.125
e.g., initRTO = 1sec
e.g., we multiple RTTVAR by 4

## Slide 118: Magic Numbers
Where do the constants in the RTO mechanism come from?
 e.g., alpha = 0.125
e.g., initRTO = 1sec
e.g., we multiple RTTVAR by 4
Rough consensus …
but, it still stinks
We strive for mechanisms that do not require magic constants